## Slide 1
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
1 / 7
AI-Enhanced Agent-Based
Decision Support for
Transboundary WEFE Resilience
An interactive decision experiment
Attlee M. GAMUNDANI
Fungai BHUNU SHAVA and Simon MUCHINENYIKA
27th WaterNet / WARFSA / GWPSA Symposium
Arusha, Tanzania 28–30 October 2026

## Slide 2
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
2 / 7
The monthly decision mechanism
Actor response changes planned demand. The policy allocates limited water and pumping energy.
01
Read inflow and available energy
02
Update farm demand using previous shortage
03
Apply a policy within the resource constraints
04
Record sector deliveries and residual flow
Q = total deliveries + residual flow
Next farm demand = baseline × (1 − α × previous deficit)

## Slide 3
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P3 Reserve flow
Inflow 65 Energy 28 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 11.43 | 42.9%
Farm 1 | 30.00 | 16.07 | 46.4%
Farm 2 | 20.00 | 10.71 | 46.4%
Pumping energy
28.00 / 28.00
Residual flow
26.79 / 25.00 target
A change in policy changes the distribution of unmet demand.

## Slide 4
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
4 / 7
Shortage changes the next month’s demand
A fixed seed-7 trajectory, with drought in months 25–36 and 30% less pumping energy
Month 25
Month 26
26 no feedback
Month 25 Q 50.39 E 28.00
Adaptation α = 0.25
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Farm deficit | 25 | 20 | 21.0526 | 20.8333 | 20.8791 | 20.8696 | 20.8716 | 20.8711 | 25.6855 | 31.8271 | 18.5165 | 21.3596 | 20.7691 | 20.8925 | 20.8668 | 20.8721 | 20.871 | 20.8713 | 20.8712 | 20.8712 | 39.9237 | 24.8503 | 33.1632 | 18.2198 | 88.7016 | 75.5022 | 81.8344 | 65.67 | 67.6033 | 75.2506 | 97.1063 | 100 | 100 | 100 | 100 | 100 | 0 | 25 | 20 | 21.0526 | 20.8333 | 20.8791 | 20.8696 | 20.8716 | 20.8711 | 42.4696 | 16.091 | 21.8565 | 20.665 | 20.9142 | 20.8622 | 20.8731 | 20.8708 | 20.8713 | 20.8712 | 20.8712 | 21.1943 | 20.8037 | 20.8853 | 20.8683
Municipal deficit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.9719 | 30.5328 | 35.1105 | 5.04 | 10.0942 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Agent | Demand | Supply | Next
Town | 20.00 | 20.00 | 20.00
Farm 1 | 28.63 | 3.24 | 23.35
Farm 2 | 19.09 | 2.16 | 15.56
Farm 1 next demand
30 × (1 − 0.25 × 0.89) = 23.35
Deficit severity (%) by month

## Slide 5
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
5 / 7
An emulator with a measurable error
k-nearest neighbours, k = 20, predicts the 60-month mean farm deficit
Familiar grid
Severe held out
Severe familiar
Drought 0.5 Energy 40 P4 Municipal protection
34.5%
kNN prediction
34.4%
Held-out test mean, 30 seeds
Selected scenario | Value
Exact scenario lookup | 34.3%
Difference from test mean | 0.088 pp
Training trajectories | 2,520
Full benchmark MAE | pp
Lookup, familiar grid | 0.142
kNN, familiar grid | 0.153
kNN, severe held out | 3.055

## Slide 6
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
6 / 7
Namibia in shared river systems
Proposed decision units within two separate basin configurations
NAMIBIA
Cubango-Okavango
OKACOM institutional context
Allocation
Boundary inflow
Downstream residual flow
Orange-Senqu
ORASECOM institutional context
Allocation
Boundary inflow
Downstream residual flow
National testing scope with transboundary inflow and downstream accounting

## Slide 7
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Restart
7 / 7
Municipal protection shifts shortage to farms
A policy comparison makes the distribution of scarcity visible
Chart: 
| Farms | Municipality
P3 Reserve flow | 33.0783 | 15.0876
P4 Municipal protection | 37.0763 | 3.7235
−11.36 pp
Municipal deficit
+4.00 pp
Farm deficit
Pooled synthetic benchmark. Mean deficit severity (%), 900 trajectories per policy.
Delivered
Allocation model, farm-agent feedback, AI evaluation and inspectable outcomes

## Slide 8
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P4 Municipal protection
Inflow 65 Energy 28 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 20.00 | 0.0%
Farm 1 | 30.00 | 12.00 | 60.0%
Farm 2 | 20.00 | 8.00 | 60.0%
Pumping energy
23.20 / 28.00
Residual flow
25.00 / 25.00 target
Municipal priority reallocates the remaining shortage to farms.

## Slide 9
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P4 Municipal protection
Inflow 90 Energy 15 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 20.00 | 0.0%
Farm 1 | 30.00 | 6.88 | 77.1%
Farm 2 | 20.00 | 4.58 | 77.1%
Pumping energy
15.00 / 15.00
Residual flow
58.54 / 25.00 target
Municipal priority reallocates the remaining shortage to farms.

## Slide 10
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P4 Municipal protection
Inflow 20 Energy 28 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 0.00 | 100.0%
Farm 1 | 30.00 | 0.00 | 100.0%
Farm 2 | 20.00 | 0.00 | 100.0%
Pumping energy
0.00 / 28.00
Residual flow
20.00 / 25.00 target
Inflow is below the environmental target.

## Slide 11
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P4 Municipal protection
Inflow 120 Energy 70 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 20.00 | 0.0%
Farm 1 | 30.00 | 30.00 | 0.0%
Farm 2 | 20.00 | 20.00 | 0.0%
Pumping energy
52.00 / 70.00
Residual flow
50.00 / 25.00 target
Municipal priority reallocates the remaining shortage to farms.

## Slide 12
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P1 Priority
Inflow 65 Energy 28 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 20.00 | 0.0%
Farm 1 | 30.00 | 17.14 | 42.9%
Farm 2 | 20.00 | 8.57 | 57.1%
Pumping energy
28.00 / 28.00
Residual flow
19.29 / 25.00 target
A change in policy changes the distribution of unmet demand.

## Slide 13
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
3 / 7
Where does the shortage go?
Prepared allocation scenarios with identical demands and explicit resource constraints
Scenario choices
Worked P3
Worked P4
Low energy
Severe scarcity
Abundant supply
P1 Priority
P2 Proportional
P2 Proportional
Inflow 65 Energy 28 Environmental target 25
Agent | Demand | Delivery | Deficit
Municipality | 20.00 | 18.57 | 7.1%
Farm 1 | 30.00 | 15.18 | 49.4%
Farm 2 | 20.00 | 10.12 | 49.4%
Pumping energy
28.00 / 28.00
Residual flow
21.13 / 25.00 target
A change in policy changes the distribution of unmet demand.

## Slide 14
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
4 / 7
Shortage changes the next month’s demand
A fixed seed-7 trajectory, with drought in months 25–36 and 30% less pumping energy
Month 25
Month 26
26 no feedback
Month 26 Q 54.53 E 28.00
Adaptation α = 0.25
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Farm deficit | 25 | 20 | 21.0526 | 20.8333 | 20.8791 | 20.8696 | 20.8716 | 20.8711 | 25.6855 | 31.8271 | 18.5165 | 21.3596 | 20.7691 | 20.8925 | 20.8668 | 20.8721 | 20.871 | 20.8713 | 20.8712 | 20.8712 | 39.9237 | 24.8503 | 33.1632 | 18.2198 | 88.7016 | 75.5022 | 81.8344 | 65.67 | 67.6033 | 75.2506 | 97.1063 | 100 | 100 | 100 | 100 | 100 | 0 | 25 | 20 | 21.0526 | 20.8333 | 20.8791 | 20.8696 | 20.8716 | 20.8711 | 42.4696 | 16.091 | 21.8565 | 20.665 | 20.9142 | 20.8622 | 20.8731 | 20.8708 | 20.8713 | 20.8712 | 20.8712 | 21.1943 | 20.8037 | 20.8853 | 20.8683
Municipal deficit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.9719 | 30.5328 | 35.1105 | 5.04 | 10.0942 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Agent | Demand | Supply | Next
Town | 20.00 | 20.00 | 20.00
Farm 1 | 23.35 | 5.72 | 24.34
Farm 2 | 15.56 | 3.81 | 16.22
Farm 1 next demand
30 × (1 − 0.25 × 0.76) = 24.34
Deficit severity (%) by month

## Slide 15
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
4 / 7
Shortage changes the next month’s demand
A fixed seed-7 trajectory, with drought in months 25–36 and 30% less pumping energy
Month 25
Month 26
26 no feedback
Month 26 Q 54.53 E 28.00
Adaptation α = 0
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Farm deficit | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 29.5631 | 36.2047 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 43.0584 | 32.3509 | 37.3155 | 25 | 89.2162 | 80.9347 | 85.2633 | 72.6935 | 72.922 | 79.4335 | 97.6507 | 100 | 100 | 100 | 100 | 100 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 45.4714 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25.3062 | 25 | 25 | 25
Municipal deficit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.9719 | 30.5328 | 35.1105 | 5.04 | 10.0942 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Agent | Demand | Supply | Next
Town | 20.00 | 20.00 | 20.00
Farm 1 | 30.00 | 5.72 | 30.00
Farm 2 | 20.00 | 3.81 | 20.00
Farm 1 next demand
30 × (1 − 0 × 0.81) = 30.00
Deficit severity (%) by month

## Slide 16
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
5 / 7
An emulator with a measurable error
k-nearest neighbours, k = 20, predicts the 60-month mean farm deficit
Familiar grid
Severe held out
Severe familiar
Drought 0.35 Energy 40 P4 Municipal protection
34.5%
kNN prediction
37.4%
Held-out test mean, 30 seeds
Selected scenario | Value
Exact scenario lookup | Unavailable
Difference from test mean | 2.921 pp
Training trajectories | 1,680
Full benchmark MAE | pp
Lookup, familiar grid | 0.142
kNN, familiar grid | 0.153
kNN, severe held out | 3.055

## Slide 17
SMART WEFE
INNOVATION MODEL
SWIM RESEARCH
PROTOTYPE
01 Opening
02 Mechanism
03 Allocation
04 Agent response
05 AI evaluation
06 Namibia
07 Deliverable
10-minute talk
Preset scenarios
Synthetic research prototype / Normalized units
Back
Continue
5 / 7
An emulator with a measurable error
k-nearest neighbours, k = 20, predicts the 60-month mean farm deficit
Familiar grid
Severe held out
Severe familiar
Drought 0.35 Energy 40 P4 Municipal protection
37.3%
kNN prediction
37.4%
Held-out test mean, 30 seeds
Selected scenario | Value
Exact scenario lookup | 37.3%
Difference from test mean | 0.124 pp
Training trajectories | 2,520
Full benchmark MAE | pp
Lookup, familiar grid | 0.142
kNN, familiar grid | 0.153
kNN, severe held out | 3.055